## Slide 1: In-situ OAM (IOAM)
November 11-12 2017
IETF 100 Hackathon
https://tools.ietf.org/html/draft-ietf-ippm-ioam-data

## Slide 2: Team
Aditya Dogra @ Cisco << First time at hackathon and IETF
Kai Lu @Huawei
Manish Kumar (Remote) @ Fire eye << First time at hackathon
Mickey Spiegel @ Barefoot << First time at hackathon
Shwetha Bhandari @ Cisco
Yap Chern Nam @ Temasek Polytechnic

## Slide 3
Telemetry UI
Analytics and
Monitoring Engine
IOAM Reports
Metadata
Metadata
Metadata
IOAM Instr.
Payload
IOAM Instr.
Payload
Metadata
Metadata
Metadata
IOAM Instr.
Payload
Metadata
Metadata
IOAM Instr.
Payload
Metadata
In-situ OAM

## Slide 4: Benefits of IOAM
Complete network visibility
No black boxes, silent drops and guessing.
Real-time monitoring
No need to depend on polling
Per-packet metadata
No sifting through aggregated counters and information
Full line rate, zero switch CPU involvement
Not limited by control plane bandwidth
https://tools.ietf.org/html/draft-ietf-ippm-ioam-data
https://tools.ietf.org/html/draft-brockners-ioam-vxlan-gpe
https://tools.ietf.org/html/draft-brockners-inband-oam-transport

## Slide 5: Goals
Encapsulation in multiple protocols
Hardware implementation
Interop between P4 and VPP data plane

## Slide 6: Results
IPv6 implementations
  P4
  VPP
  Interop
VXLAN-GPE implementation in P4
  Performance tested on Barefoot Tofino

## Slide 7: Programmable Forwarding Plane
P4 Program
(switch.p4)
P4 Program Dependent APIs
(C-code)
Port 0
Port N
HW or SW Forwarding Plane
CPU I/F
Runtime Configuration, Notifications,
Query
P4 Compiler

## Slide 8
VPP
P4

## Slide 9: IOAM Incremental Trace on Barefoot Tofino Switch
Modified existing implementation of P4.org In-band Network Telemetry (INT) spec
Support IOAM data and transport encapsulation formats
Change in p4 code  change in HW behavior  IOAM at 6.5 Tb/s
Barefoot Tofino Switch
(6.5 Tb/s)
Queue
100G
100G
Receiver
[Enable IOAM]
Add Switch ID, Interface ID, Queue Depth, Ingress Timestamp & Transit Delay to every packet
Collect and visualize Packet headers
Sender

## Slide 10
###[ Ethernet ]###
dst = 00:11:22:33:44:55
src = 00:77:66:55:44:33
type = IPv4
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 160
id = 1
flags =
frag = 0L
ttl = 63
proto = udp
chksum = 0x5d36
src = 10.11.0.1
dst = 10.10.10.1
\options \
###[ UDP ]###
sport = 101
dport = 4790
len = 140
chksum = 0x0
###[ VXLAN_GPE ]###
flags = I+P
reserved1 = 0x0
next_proto= 0x6
vni = 4660
reserved2 = 0x0
[...]
[...]
###[ VXLAN_GPE_IOAM_header ]###
ioam_type = 0x1
length = 0x6
rsvd = 0x0
next_proto= 0x3
###[ IOAM_inc_trace_metadata_header ]###
ioam_trace_bits= 0x8200
node_len = 2L
o = 0L
l = 0L
rsvd = 0L
max_len = 127L
###[ IOAM_hop_info ]###
val = 0x3f111111L
###[ IOAM_hop_info ]###
val = 0x3L
###[ IOAM_hop_info ]###
val = 0x40222222L
###[ IOAM_hop_info ]###
val = 0x5L
[...]
[...]
##[ Ethernet ]###
dst = 00:33:33:33:33:33
src = 00:11:11:11:11:11
type = IPv4
###[ IP ]###
version = 4L
ihl = 5L
tos = 0x0
len = 86
id = 108
flags =
frag = 0L
ttl = 64
proto = tcp
chksum = 0x7431
src = 2.2.2.2
dst = 1.1.1.1
\options \
###[ TCP ]###
sport = 1234
dport = http
seq = 0
ack = 0
dataofs = 5L
reserved = 0L
flags = S
window = 8192
chksum = 0x887a
urgptr = 0
options = []
###[ Raw ]###
load = '\x00\x01\x02\x03\x04\x05\x06\x07\x08\t\n\x0b\x0c\r\x0e\x0f\x10\x11\x12\x13\x14\x15\x16\x17\x18\x19\x1a\x1b\x1c\x1d\x1e\x1f !"#$%&\'()*+,-'

## Slide 11: Source code
https://github.com/vpp-dev/vpp.git - ioam-ietf100
P4 program git
Scripts to create p4 simple switch + vpp setup

## Slide 12: Feedback on draft-ietf-ippm-ioam-data
Proposed encaps are feasible in both hardware and software implementations
5 issues raised
  IOAM-Trace-Type undefined bits: clarify behavior for future compatibility
  IOAM Incremental Trace Max Length Definition
  Queue ID and Queue Depth
  Checksum complement effect on sink nodes?
  Transit Delay O bit: Is it really necessary?
Ease of building open source dataplane reference implementation in VPP and P4